## Slide 1: CardioTwin Sentinel
DIGITAL TWIN CHALLENGE 2026 · HAPPIEST HEALTH
A ₹1,165 cardiac digital twin that learns your heart's own baseline
Team Root Access (Solo)
Harsh Mishra · Visvesvaraya National Institute of Technology, Nagpur
Screening, not diagnosis. The clinician decides.
Notes: OPEN (about 1 min) - Name, team Root Access (solo), VNIT Nagpur, Digital Twin Challenge 2026 by Happiest Health. - One-line pitch: a ₹1,165 device that learns your heart's own baseline, screens 8 rhythm classes with explainable AI, and projects 10-year risk. - Set the frame early: this is screening and decision support, not diagnosis.

## Slide 2: India's heart disease crisis has no affordable, intelligent screening tool
THE PROBLEM
28%
of all deaths in India are cardiovascular
10–15 yrs
earlier onset in South Asians than in Western populations
160,000+
Health & Wellness Centres with no affordable cardiac screening
WHAT EXISTS TODAY
Apple Watch
₹41,900+
24–48 h Holter monitor
₹5,000–12,000 / rental
Hospital bedside monitor
₹1.2–3.5 lakh
Pulse oximeter: one number, no memory
₹600–1,200
BUILT FOR
Community Health Officers at Ayushman Bharat centres
2-minute seated check · live rhythm screening · FHIR referral to e-Sanjeevani
Notes: PROBLEM (about 1.5 min) - 28% of deaths in India are cardiovascular; South Asians are hit 10–15 years earlier than Western populations. - There are 160,000+ Ayushman Bharat Health & Wellness Centres in rural and semi-urban India, but no affordable, intelligent screening tool for them. - Walk the price list: smartwatch ₹41,900+, Holter ₹5,000–12,000 per rental, bedside monitor ₹1.2–3.5 lakh, pulse oximeter ₹600–1,200 but with zero memory or intelligence. - Who uses ours: a Community Health Officer. Two-minute seated check, live screening, and a FHIR report to refer through e-Sanjeevani.

## Slide 3: One ₹1,165 device. Five stages. Every result explained
OUR SOLUTION
01
Hardware Edge
ESP32 + MAX30102 sampling at 100 Hz
02
Signal Gate
Blocks noise, keeps real arrhythmia
03
Dual-Modality AI
Classical + CNN, 8 rhythm classes
04
Digital Twin
Personal baseline + 10-year risk
05
Clinician View
Live dashboard + FHIR R4 export
Data flow: I2C → WiFi TCP / JSON → clean 10 s windows → rhythm + SHAP → REST + WebSocket → FHIR R4
The live pulse says what is happening now. The patient record says what it means for the next 10 years.
Notes: SOLUTION (about 1.5 min) - this is the one-glance architecture; the architecture PDF has the detail. - Walk left to right: hardware edge, signal gate, dual-modality AI, digital twin, clinician view. - Two streams: live optical pulse (stages 1–3) and the patient EHR, which joins at the digital twin. - Protocols along the way: I2C inside the node, WiFi TCP/JSON to the backend, REST + WebSocket to the dashboard, FHIR R4 out to ABDM.

## Slide 4: A ₹1,165 node built around a hard 100 Hz deadline
STAGE 1 · HARDWARE EDGE
₹1,165
about $14 per unit
35× cheaper than an Apple Watch
CORE 1
Samples the optical sensor at exactly 100 Hz
10,000 µs hardware timer
CORE 0
Streams JSON over WiFi and drives the OLED
Never stalls sampling
MAX30102 · 18-bit optical sensor
SSD1306 OLED · live BPM and SQI
6–8 h battery
About 60 g
Every chunk carries a boot ID, a sequence number and microsecond timestamps, so drift and dropped data are detectable.
Notes: HARDWARE (about 1.5 min) - hold up the device if you can. - ₹1,165 total (about $14): ESP32 ₹480, MAX30102 ₹220, OLED ₹140, power ₹210, passives and finger clip ₹115. Under ₹950 in a 1,000-unit batch. - Why dual-core: Core 1 owns the 10 ms sampling deadline via a hardware timer; Core 0 handles WiFi, JSON and the OLED, so network hiccups never distort the waveform. - Each chunk carries device_boot_id, seq and microsecond timestamps so the gate can detect jitter and drift.

## Slide 5: Noise is blocked. Arrhythmia is not
STAGE 2 · SIGNAL RELIABILITY GATE
BLOCKS THE AI
The measurement failed
Finger off (ADC below 20k)
Amplifier saturation (ADC above 260k)
Timing jitter above 20%
Low signal quality (SQI below 0.40)
PASSES TO THE AI
The physiology is real
AFib-type irregular pulse
Heart rate below 40 or above 180 BPM
Flagged for clinical review, never discarded as noise
100%
finger-off rejection
≤ 2.0 BPM
error vs reference pulse
0
persistent false alarms in validation scenarios
Notes: SIGNAL GATE (about 1.5 min) - Most pipelines throw away anything irregular as noise, which also throws away the arrhythmias you are trying to find. - Here the gate is decoupled: only failures of the measurement itself block the AI (finger off, saturation, timing jitter, SQI below 0.40). - Genuine irregularity (AFib-type rhythm, extreme rates below 40 or above 180 BPM) passes through, flagged for clinical review. - Operational validation: 100% finger-off rejection, error of 2.0 BPM or less against a reference pulse, zero persistent false alarms.

## Slide 6: Your heart, compared with your own heart
STAGE 4 · DIGITAL TWIN
1
Sit for 2 minutes
At least 6 clean 10-second windows of seated rest
2
Learn your fingerprint
Median and MAD of BPM, RR variability and RMSSD
3
Score every departure
Instability Index 0–100, smoothed with EMA (α = 0.35)
No baseline, no score.
Uncalibrated users see "Personal baseline required" instead of a guess from population averages. Baselines expire after 30 days or when the device changes.
Notes: PERSONAL BASELINE (about 2 min) - the core idea of the digital twin. - Resting pulse varies enormously between people (an athlete near 48 BPM, a hypertensive patient near 84), so a fixed 72 BPM norm is wrong for most people. - Calibration: two minutes seated, at least 6 clean 10-second windows. We store Median and MAD, which resist outlier spikes, instead of mean and standard deviation. - Scoring: robust z-score = |reading − median| / (1.4826 × MAD), blended into a 0–100 Instability Index: rhythm distress, RMSSD below 25 ms, BPM above 105, smoothed by EMA with α = 0.35. - Without a baseline the score is null and the dashboard says "Personal baseline required". Baselines expire at 30 days or if the device or sensor configuration changes.

## Slide 7: Two ways of seeing one heartbeat, fused into one answer
STAGE 3 · DUAL-MODALITY AI
CLASSICAL
27 biomarkers
XGBoost + Random Forest + ExtraTrees
DEEP LEARNING
Raw 1,000-sample waveform
Inception-1D CNN · 4 kernel sizes · 393k params
FUSION
0.38 | 0.62
classical | CNN
8 RHYTHM CLASSES
Normal
Tachycardia
Bradycardia
AFib
Cardiac paced
V. tachycardia
V. flutter / fib
Asystole
Hand-built HRV statistics capture physiology. The CNN captures waveform shape the statistics miss.
Notes: DUAL-MODALITY AI (about 2 min) - Modality A: 27 biomarkers (time-domain HRV such as RMSSD, SDNN, pNN50; morphology; Welch spectral LF/HF) into an XGBoost + Random Forest + ExtraTrees soft-voting ensemble. - Modality B: Inception-1D CNN on the raw 1,000-sample, 100 Hz window; four parallel kernel sizes (3, 7, 15, 31) with residual connections; 393,224 parameters; about 4.2 ms on CPU. - Fusion: 0.38 × classical + 0.62 × CNN. These weights were chosen by inner-fold search inside nested cross-validation, not on test data. - Output: 8 classes - Normal, Tachycardia, Bradycardia, AFib, Cardiac paced, V. tachycardia, V. flutter/fib, Asystole.

## Slide 8: Every alert says why, and says what it does not know
EXPLAINABLE BY DESIGN
TOP BIOMARKERS DRIVING PREDICTIONS (MEAN |SHAP|)
Chart: 
| sig_skew | peak_amp_mean | rr_mean | bpm | pnn50
Mean ¦SHAP¦ | 0.4895 | 0.4271 | 0.3646 | 0.3524 | 0.2201
EVIDENCE LEDGER
Machine-readable limits shipped with every result
No SpO₂ measurement
PPG is not a 12-lead ECG
Trained on ICU-heavy data
Plain-language reasons: BPM, RR-CV and RMSSD deviation, with duration.
Notes: EXPLAINABILITY (about 1.5 min) - SHAP TreeExplainer runs on the 27 biomarkers. Globally the top drivers are signal skew, mean peak amplitude, mean RR interval and BPM. - For AFib the drivers are RR variability, pNN50 and RMSSD (irregular-irregular rhythm). For tachycardia: compressed RR intervals and high BPM. - Each result also carries a plain-language reason (deviation in BPM, RR-CV and RMSSD with temporal duration). - The Evidence Ledger is machine-readable and states what the system does NOT know: no SpO₂, not a 12-lead ECG, ICU-heavy training data.

## Slide 9: From today's pulse to a 10-year plan
STAGE 4 · DIGITAL TWIN
SAME PATIENT, TWO 10-YEAR RISK ESTIMATES
16.8%
24.4%
Standard Framingham vs South Asian recalibration, ×1.45
Crosses the 20% high-risk line, so statin and blood-pressure therapy are not missed.
52-year-old male smoker, SBP 145, TC 220, HDL 38
WHAT-IF: PROJECTED RELATIVE RISK REDUCTION
Beta-blockade
15–22%
High-intensity statin
22–28%
Antihypertensives
28–34%
Smoking cessation
40–50%
Combined protocol
55–68%
Educational projections assuming 5–10 years of adherence. Smoking cessation benefit measured over 5 years.
Notes: RISK ENGINE AND WHAT-IF (about 1.5 min) - Stream 1 is the patient record: age, sex, SBP (treated or not), total cholesterol, HDL, smoking, diabetes into a sex-specific Framingham Cox model (D'Agostino 2008). - Standard Framingham underestimates South Asian risk, so we apply a 1.45× recalibration (ACC/AHA treats South Asian ancestry as a risk-enhancing factor). - Example: a 52-year-old male smoker goes from 16.8% to 24.4%, crossing the 20% high-risk threshold. - What-If simulator: relative risk reductions of 15–22% (beta-blockade), 22–28% (statin), 28–34% (antihypertensives), 40–50% (smoking cessation, 5 years), 55–68% for the combined protocol. Say clearly these are educational projections.

## Slide 10: One patient, from finger-on to referral
LIVE DEMO
1
Calibrate
Two-minute seated baseline: "Personal baseline required" becomes a live score
2
Monitor
Live waveform, signal gate and Instability Index, with SHAP reasons
3
Break it
Finger-off blocks the AI. An AFib episode passes through, flagged
4
Plan and export
Change SBP, statin and smoking in What-If, then export the FHIR bundle
On-screen tags always show the data source: [LIVE_HARDWARE] · [RECORDED_REPLAY] · [SIMULATION]
Notes: DEMO RUN-OF-SHOW (record about 8–10 min live; this slide is your cue card) 1. CALIBRATE - Open Home. Show the uncalibrated state ("Personal baseline required"). Put your finger on the MAX30102, do the 2-minute seated calibration, show the baseline appear. 2. MONITOR - Live Check tab: oscilloscope waveform, 100 Hz and jitter readout, signal gate status, Instability Index, SHAP 'why' panel, dual-engine status. 3. BREAK IT - Lift your finger: gate blocks the AI ("measurement unreliable"). Then run the AFib episode scenario: it passes the gate and is flagged for clinical review. Optionally show motion-artifact and stress-tachycardia scenarios. 4. PLAN AND EXPORT - Open the What-If tab: change SBP, statin, smoking cessation and show the risk drop. Show the Twin Profile and vascular age. Export the FHIR R4 bundle. Tip: point at the provenance tag on screen so viewers know whether data is live hardware, replay or simulation. Say "screening, not diagnosis" once during the demo.

## Slide 11: 53.92% Macro-F1 on patients the model has never seen
OUTCOME
8-CLASS MACRO-F1 (RANDOM GUESS = 12.5%)
Chart: 
| Random guess | Classical ensemble | Inception-1D CNN | Nested fusion
Macro-F1 | 12.5 | 48 | 51.81 | 53.92
+5.9 pts
over the classical ensemble
+2.1 pts
over Inception-1D alone
Patient-isolated nested 5-fold CV · 2,271 patients · 4,683 windows
Notes: RESULTS (about 2 min) - These are patient-isolated numbers: StratifiedGroupKFold grouped on patient IDs, so no patient appears in both train and test; scalers are fit on training folds only; fusion weights are tuned in inner folds. - 2,271 patients, 4,683 10-second windows from MIMIC-III-Ext-PPG, CinC 2015, BUT PPG and BIDMC. - Random guess is 12.5%. Classical ensemble 48.00%, Inception-1D CNN 51.81%, nested fusion 53.92% (accuracy 59.21%, balanced accuracy 57.46%). - Fusion adds 5.9 points over classical and 2.1 over the CNN alone. 95% confidence interval about ±5 points, so frame it as a screening prototype, not a finished classifier. - Optional: the architecture tournament (Inception-1D 51.81%, ResNet-1D 49.44%, Standard 1D-CNN 49.16%, CRNN-BiLSTM 45.04%) explains why Inception-1D was chosen.

## Slide 12: Strong where signals are clear, honest where they are not
OUTCOME
F1 BY RHYTHM CLASS (DUAL FUSION)
Chart: 
| Normal | Bradycardia | Tachycardia | AFib | Asystole | V. flutter / fib | Cardiac paced | V. tachycardia
F1 | 79.33 | 67.82 | 65.29 | 53.91 | 48.37 | 47.85 | 35.32 | 33.49
WHAT WE DISCLOSE
5 of 8 classes come from a single dataset
77.08%
accuracy of guessing the dataset from biomarkers alone
So outputs are screening guidance, limits are in the Evidence Ledger, and V. tachycardia triggers ECG review.
Notes: HONEST LIMITS (about 1.5 min) - this slide builds trust with expert judges, so do not rush it. - Strongest: Normal 79.3% F1, Bradycardia 67.8%, Tachycardia 65.3%. AFib 53.9%. - Weakest: V. tachycardia 33.5% and Cardiac paced 35.3%: the hardest single-lead optical cases. - Source confounding: AFib and Cardiac paced come only from MIMIC; V. tachycardia, V. flutter/fib and Asystole only from CinC 2015. A classifier can predict which dataset a window came from at 77.08% accuracy (81.30% balanced), so the model may partly learn acquisition signatures. - We disclosed it instead of hiding it: it is in the machine-readable Evidence Ledger and the output is framed as screening guidance, with ECG review for ventricular findings. - Roadmap: multi-lead ECG, SpO₂ channel, federated learning across centres, active learning from clinician feedback.

## Slide 13: Plugs into ABDM today, and keeps patient data at the edge
BUILT FOR INDIA'S HEALTH STACK
CardioTwin session
FHIR R4 Bundle
ABHA · ABDM
e-Sanjeevani tele-consult
Heart rate LOINC 8867-4 · RMSSD LOINC 80404-7 · 10-yr risk LOINC 79423-0 · Rhythm SNOMED CT
Raw waveform stays in RAM
Rolling buffer, purged once features are computed
Only aggregates leave
27 biomarkers and departure flags, never raw signal
DPDP Act 2023 aligned
Pseudonymised IDs, baselines expire after 30 days
Notes: INTEROPERABILITY AND PRIVACY (about 1.5 min) - Every session, baseline and What-If scenario exports as an HL7 FHIR R4 Bundle linked to the 14-digit ABHA ID: heart rate LOINC 8867-4, RMSSD LOINC 80404-7, pulse rhythm SNOMED CT 361137007, 10-year risk as a RiskAssessment (LOINC 79423-0), and the ESP32 as a Device resource. - This plugs into ABDM and e-Sanjeevani tele-consultation, so a Community Health Officer can refer without paperwork. - Privacy is edge-first and aligned with the DPDP Act 2023: raw 100 Hz waveforms live only in a rolling RAM buffer; only aggregate features and departure flags are transmitted; patient handles are pseudonymised; baselines expire after 30 days. - Be ready for the question of where inference runs, because the CNN reads the raw window.

## Slide 14: Affordable. Personal. Explainable. Honest
THE TAKEAWAY
ESP32 · MAX30102
Python 3.11 · Flask · Socket.IO
PyTorch · XGBoost · SHAP
React 19 · HL7 FHIR R4
Open source under the MIT License
github.com/Harsh-15771/IoT-Arrhythmia-Detection
Team Root Access (Solo)
Harsh Mishra · VNIT Nagpur
Screening, not diagnosis. The clinician decides.
Notes: CLOSE (about 1 min) - Four words: affordable (₹1,165), personal (learns your own baseline), explainable (SHAP and the Evidence Ledger), honest (patient-isolated metrics and disclosed limits). - Stack in one line: ESP32 FreeRTOS firmware, Python/Flask backend, PyTorch + XGBoost + SHAP, React 19 dashboard, FHIR R4 export. - Open source under the MIT License; the repo link is on screen. - End on the principle: screening, not diagnosis. The clinician decides.